## Slide 1: Multiplication of Two floating point numbers
The multiplication of two floating-point numbers requires that we multiply the mantissas and add the exponents.
No comparison of exponents or alignment of mantissas is necessary.
The multiplication of the mantissas is performed in the same way as in fixed-point to provide a double-precision product.
The multiplication algorithm can be subdivided into four parts:
1. Check for zeros.
2. Add the exponents.
3. Multiply the mantissas.
4. Normalize the product.
Steps 2 and 3 can be done simultaneously if separate adders are available for the mantissas and exponents.

## Slide 2: Flowchart: Multiplication of floating point numbers
The two operands are checked to determine if they contain a zero. If either operand is equal to zero, the product in the AC is set to zero and the operation is terminated. If neither of the operands is equal to zero, the process continues with the exponent addition.
The exponent of the multiplier is in q and the adder is between exponents a and b. It is necessary to transfer the exponents from q to a, add the two exponents, and transfer the sum into a.
Since both exponents are biased by the addition of a constant, the exponent sum will have double this bias. The correct biased exponent for the product is obtained by subtracting the bias number from the sum.
The multiplication of the mantissas is done as in the fixed-point case with the product residing in A and Q . Overflow cannot occur during multiplication, so there is no need to check for it.
The product may have an underflow, so the most significant bit in A is checked. If it is a 1, the product is already normalized. If it is a 0, the mantissa in AQ is shifted left and the exponent decremented.