## Slide 1: Instruction Formats
The format of an instruction is usually depicted in a rectangular box symbolizing the bits of the instruction as they appear in memory words or in a control register. The bits of the instruction are divided into groups called fields. The most common fields found in instruction formats are:
Instruction Format
1. An operation code field that specifies the operation to be performed.
2. An address field that designates a memory address or a processor register.
3. A mode field that specifies the way the operand or the effective address is determined.
The operation code field of an instruction is a group of bits that define various processor operations, such as add, subtract, complement, and shift.
The bits that define the mode field of an instruction code specify a variety of alternatives for choosing the operands from the given address.

## Slide 2: Types of Instruction Format
The number of address fields in the instruction format of a computer depends on the internal organization of its registers. Most computers fall into one of three types of CPU organizations:
1. General register organization.
2. Single accumulator organization
3. Stack organization.
To illustrate the influence of the number of addresses on computer programs, we will evaluate the arithmetic statement
X = (A + B) • (C + D)
using zero, one, two, or three address instructions. We will use the symbols ADD, SUB, MUL, and DIV for the four arithmetic operations; MOV for the transfer-type operation; and LOAD and STORE for transfers to and from memory and AC register.
We will assume that the operands are in memory addresses A, B, C, and D, and the result must be stored in memory at address X.

## Slide 3
1. Three-Address Instructions: Computers with three-address instruction formats can use each address field to specify either a processor register or a memory operand. The program in assembly language that evaluates is shown below, together with comments that explain the register transfer operation of each instruction.
X = (A + B) × (C + D)
A D D R 1 , A , B R 1 <--M [ A ] + M [ B ]
A D D R 2 , C , D R 2 <--M [ C ] + M [ D ]
M U L X , R 1 , R 2 M [ X ] <--R 1 × R 2
It is assumed that the computer has two processor registers, R 1 and R2. The symbol M [A] denotes the operand at memory address symbolized by A .

## Slide 4
2. Two-Address Instructions: Two-address instructions are the most common in commercial computers. Here again each address field can specify either a processor register or a memory word. The program to evaluate X = (A + B) × (C + D) is as follows:
M O V R 1 , A R 1 <--M [ A ]
A D D R 1 , B R 1 <--R 1 + M [ B ]
M O V R 2 , C R 2 <--M [ C ]
A D D R 2 , D R 2 <--R 2 + M [ D ]
M U L R 1 , R 2 R 1 <--R 1 • R 2
M O V X , R 1 M [ X ] <--R 1
The MOV instruction moves or transfers the operands to and from memory and processor registers. The first symbol listed in an instruction is assumed to be both a source and the destination where the result of the operation is transferred.

## Slide 5
3. One-Address Instructions: One-address instructions use an implied accumulator (AC) register for all data manipulation. For multiplication and division there is a need for a second register. However, here we will neglect the second register and assume that the AC contains the result of all operations. The program to evaluate X = (A + B) × (C + D) is
L O A D A A C <- M [A]
A D D B A C <- A C + M [ B ]
S T O R E T M [ T ] <- A C
L O A D C A C <- M [ C ]
A D D D A C <- A C + M [ D ] C+D
M U L T A C <- A C × M [ T ]
S T O R E X M [ X ] <- A C
All operations are done between the AC register and a memory operand. T is the address of a temporary memory location required for storing the intermediate result.

## Slide 6
4. Zero-Address Instructions: A stack-organized computer does not use an address field for the instructions ADD and MUL. The PUSH and POP instructions, however, need an address field to specify the operand that communicates with the stack. The following program shows how X = (A + B) × (C + D) will be written for a stack organized computer. (TOS stands for top of stack.)
P U S H A T O S <- A
P U S H B T O S <- B
A D D T O S <- ( A + B )
P U S H C T O S <- C
P U S H D T O S <- D
A D D T O S <- ( C + D )
M U L T O S <- ( C + D ) • ( A + B )
P O P X M [ X ] <- T O S

## Slide 7: RISC Instructions
The instruction set of a typical RISC processor is restricted to the use of load and store instructions when communicating between memory and CPU. All other instructions are executed within the registers of the CPU without referring to memory.
A program for a RISC-type CPU consists of LOAD and STORE instructions that have one memory and one register address, and computational-type instructions that have three addresses with all three specifying processor registers. The following is a program to evaluate
X = (A + B) × (C + D)
L O A D R 1 , A R 1 <--M [ A ]
L O A D R 2 , B R 2 <--M [ B ]
L O A D R3 , C R3 <--M [ C ]
L O A D R4, D R4 <--M [ D ]
A D D R 1 , R 1 , R 2 R 1 <--R 1 + R 2
A D D R 3 , R 3 , R 4 R 3 <--R 3 + R 4;
M U L R 1 , R 1 , R 3 R 1 <--R 1 × R 3
S T O R E X , R 1 M [ X ] <--R 1
The load instructions transfer the operands from memory to CPU registers.

## Slide 8
Write a program to evaluate the arithmetic statement
X: = (A-B)+(C*(D*E-F))/ (G+H*K)
3 Address
SUB R1,A,B R1<-M[A]-M[B]
MUL R2,D,E R2<-M[D]*M[E]
SUB R2,R2,F R2<-R2-M[F]
MUL R2,C,R2 R2<-M[C]*R2
ADD R1,R1,R2 R1<-R1+R2 // A-B+C*(D*E-F)
MUL R3,H,K R3<-M[H]*M[K]
ADD R3,R3,G R3<-R3+M[G]
DIV X,R1,R3 M[X]<-R1/R3 //A-B+C*(D*E-F)/ (G+H*K)

## Slide 9
2 Address : X: = (A-B)+(C*(D*E-F))/ (G+H*K)
MOV R1,A R1<-M[A]
SUB R1,B R1<-R1-M[B]
MOV R2,D R2<-M[D]
MUL R2,E R2<-R2*M[E]
SUB R2,F R2<-R2-M[F]
MUL R2,C R2<-R2*M[C]
ADD R1,R2 R1<-R1+R2
MOV R3,H R3<-M[H]
MUL R3,K R3<-R3*M[K]
ADD R3,G R3<-R3+M[G]
DIV R1,R3 R1<-R1/R3
MOV X,R1 M[X]<-R1

## Slide 10
One Address: X: = (A-B)+(C*(D*E-F))/ (G+H*K)
LOAD A AC<-M[A]
SUB B AC<-AC-M[B]
STORE T M[T]<-AC //A-B
LOAD D AC<-M[D]
MUL E AC<-AC*M[E] //D*E
SUB F AC<-AC-M[F] //D*E-F
MUL C AC<-AC*M[C] //C*(D*E-F)
ADD T AC<-AC+M[T]
STORE T M[T]<-AC //A-B+C*(D*E-F)
LOAD H AC<-M[H]
MUL K AC<-AC*M[K]
ADD G AC<-AC+M[G]
STORE T1 M[T1]<-AC // (G+H*K)
LOAD T AC<-M[T]
DIV T1 AC<-AC/M[T1] // A-B+C*(D*E-F)/ (G+H*K)
STORE X M[X]<-AC //X: = A-B+C*(D*E-F)/ (G+H*K)

## Slide 11
Zero Address: X: = (A-B)+(C*(D*E-F))/ (G+H*K)
=AB-CDE*F-*+GHK*+/
PUSH A TOS<-A
PUSH B TOS<-B
SUB TOS<-A-B
PUSH C TOS<-C
PUSH D TOS<-D
PUSH E TOS<-E
MUL TOS<-D*E
PUSH F TOS<-F
SUB TOS<-(D*E-F)
MUL TOS<-(C*(D*E-F))
ADD TOS<-(A-B)+(C*(D*E-F))
PUSH G TOS<-G
PUSH H TOS<-H
PUSH K TOS<-K
MUL TOS<-H*K
ADD TOS<-(G+H*K)
DIV TOS<-(A-B)+(C*(D*E-F))/(G+H*K)
POP X M[X]<-TOS