## Slide 1: Subroutine Call and Return
A subroutine is a self-contained sequence of instructions that performs a given computational task.
During the execution of a program, a subroutine may be called to perform its function many times at various points in the main program.
Each time a subroutine is called, a branch is executed to the beginning of the subroutine to start executing its set of instructions. After the subroutine has been executed, a branch is made back to the main program.
The instruction that transfers program control to a subroutine is known by different names. The most common names used are call subroutine, jump to subroutine, branch to subroutine, or branch and save address.
A call subroutine instruction consists of an operation code together with an address that specifies the beginning of the subroutine.
The instruction is executed by performing two operations:
The address of the next instruction available in the program counter (the return address) is stored in a temporary location so the subroutine knows where to return.
Control is transferred to the beginning of the subroutine.

## Slide 2
The last instruction of every subroutine, commonly called return from subroutine, transfers the return address from the temporary location into the program counter.
This results in a transfer of program control to the instruction whose address was originally stored in the temporary location.

## Slide 3: Program Interrupt
The concept of program interrupt is used to handle a variety of problems that arise out of normal program sequence.
Program interrupt refers to the transfer of program control from a currently running program to another service program as a result of an external or internal generated request.
Control returns to the original program after the service program is executed.
The interrupt procedure is, in principle, quite similar to a subroutine call except for three variations:
The interrupt is usually initiated by an internal or external signal rather than from the execution of an instruction.
The address of the interrupt service program is determined by the hardware rather than from the address field of an instruction;
An interrupt procedure usually stores all the information necessary to define the state of the CPU rather than storing only the program counter.

## Slide 4
After a program has been interrupted and the service routine been executed, the CPU must return to exactly the same state that it was when the interrupt occurred.
Only, if this happens will the interrupted program be able to resume exactly as if nothing had happened. The state of the CPU at the end of the execute cycle (when the interrupt is recognized) is determined from:
1. The content of the program counter
2. The content of all processor registers
3. The content of certain status conditions
Program Status Word: The collection of all status bit conditions in the CPU is sometimes called a program status word or PSW.
The PSW is stored in a separate hardware register and contains the status information that characterizes the state of the CPU.
It includes the status bits from the last ALU operation and it specifies the interrupts that are allowed to occur and whether the CPU is operating in a supervisor or user mode.
When the CPU is executing a program that is part of the operating system, it is said to supervisor mode be in the supervisor or system mode. Certain instructions are privileged and can be executed in this mode only.

## Slide 5
The CPU is normally in the user mode when executing user programs. The mode that the CPU is operating at any given time is determined from special status bits in the PSW.
Types of Interrupts: There are three major types of interrupts that cause a break in the normal execution of a program. They can be classified as:
1. External Interrupts: External interrupts come from input-output (I/O) devices, from a timing device, from a circuit monitoring the power supply, or from any other external source. Examples that cause external interrupts are I/O device requesting transfer of data, I/O device finished transfer of data, elapsed time of an event, or power failure. Timeout interrupt may result from a program that is in an endless loop and thus exceeded its time allocation.
2. Internal Interrupts: Internal interrupts arise from illegal or erroneous use of an instruction or data. Internal interrupts are also called traps. Examples of interrupts caused by internal error conditions are register overflow, attempt to divide by zero, an invalid operation code, stack overflow, and protection violation. These error conditions usually occur as a result of a premature termination of the instruction execution.
3. Software Interrupts: A software interrupt is initiated by executing an instruction. Software interrupt is a special call instruction that behaves like an interrupt rather than a subroutine call. It can be used by the programmer to initiate an interrupt procedure at any desired point in the program.