## Slide 1: Reduced Instruction set Computer (RISC)
A number of computer designers recommended that computers use fewer instructions with simple constructs so they can be executed much faster within the CPU without having to use memory as often.
This type of computer is classified as a reduced instruction set computer or RISC.
The RISC is a Reduced Instruction Set Computer microprocessor and its architecture includes a set of instructions that are highly customized.
The main function of this is to reduce the time of instruction execution by limiting as well as optimizing the number of commands.
So each command cycle uses a single clock cycle where every clock cycle includes three parameters namely fetch, decode & execute.
RISC reduce the cycles per instruction at the cost of the number of instructions per program.
The kind of processor is mainly used to execute several difficult commands by merging them into simpler ones.

## Slide 2: RISC Characteristics
The major characteristics of a RISC processor are:
1. Relatively few instructions.
2. Relatively few addressing modes.
3. Memory access limited to load and store instructions.
4. All operations done within the registers of the CPU.
5. Fixed-length, easily decoded instruction format.
6. Single-cycle instruction execution.
7. Hardwired rather than micro-programmed control.
8. A relatively large number of registers in the processor unit.
9. Efficient instruction pipeline
10. Compiler support for efficient translation of high-level language programs
into machine language programs.

## Slide 3: Complex Instruction Set Computer (CISC)
This processor includes a huge collection of simple to complex instructions. These instructions are specified in the level of assembly language level and the execution of these instructions takes more time.
A complex instruction set computer is a computer where single instructions can perform numerous low-level operations like a load from memory, an arithmetic operation, and a memory store or are accomplished by multi-step processes or addressing modes in single instructions, as its name proposes “Complex Instruction Set ”.
The CISC approach attempts to minimize the number of instructions per program but at the cost of increase in number of cycles per instruction.
The essential goal of a CISC architecture is to attempt to provide a single machine instruction for each statement that is written in a high-level language.
The translation from high-level to machine language programs is done by means of a compiler program. One reason for the trend to provide a complex instruction set is the desire to simplify the compilation and improve the overall computer performance.

## Slide 4: CISC Characteristics
1. A large number of instructions-typically from 100 to 250 instructions.
2. Some instructions that perform specialized tasks and are used infrequently.
3. A large variety of addressing modes-typically from 5 to 20 different modes.
4. Variable-length instruction formats.
5. Instructions that manipulate operands in memory.
6. CISC may take more time to execute the code as compared with an only clock cycle.
7. CISC supports high-level languages for simple compilation and complex data structure.
8. For writing an application, less instruction is required
9.The code length is very short, so it needs extremely small RAM.
10. It highlights the instruction on hardware while designing as it is faster to design than the software.
11. Instructions are larger as compared with a single word.
12. It gives simple programming within assembly language.