## Slide 1: Interrupt
Interrupt:- It is a special Command generated by the CPU to inform the interface to issue an interrupt request signal when the data is available for the device.
Types of Interrupt:-
External interrupts:- External interrupts come from input-output (l/0) devices, from a timing device, from a circuit monitoring the power supply, or from any other external source.
Examples: That cause external interrupts are l/0 device requesting transfer of data, l/0 device finished transfer of data, elapsed time of an event, or power failure.
2. Internal interrupts:- Internal interrupts arise from illegal or erroneous use of an instruction or data. Internal interrupts are also called traps .
Examples of interrupts caused by internal error conditions are register overflow, attempt to divide by zero, an invalid operation code, stack overflow, and protection violation. These error conditions usually occur as a result of a premature termination of the instruction execution.

## Slide 2
3. Software interrupts:- A software interrupt is initiated by executing an instruction. Software interrupt is a special call instruction that behaves like an interrupt rather than a subroutine call. It can be used by the programmer to initiate an interrupt procedure at any desired point in the program.
The most common use of software interrupt is associated with a supervisor call instruction.
This instruction provides means for switching from a CPU user mode to the supervisor mode.

## Slide 3: Priority Interrupt/Daisy Chaining
Priority Interrupt:-Determines which interrupt is to be served first when two or more requests are made simultaneously
Also determines which interrupts are permitted to interrupt the computer while another is being serviced
Higher priority interrupts can make requests while servicing a lower priority interrupt.
Daisy Chaining Priority

## Slide 4
The daisy-chaining method of establishing priority consists of a serial connection of all devices that request an interrupt.
The device with the highest priority is placed in the first position, followed by lower- priority devices up to the device with the lowest priority, which is placed last in the chain.
This method of connection between three devices and the CPU is shown in figure.
If any device has its interrupt signal in the low-level state, the interrupt line goes to the low-level state and enables the interrupt input in the CPU.
When no interrupts are pending, the interrupt line stays in the high-level state and no interrupts are recognized by the CPU.
The CPU responds to an interrupt request by enabling the interrupt acknowledge line.
This signal passes on to the next device through the PO (priority out) output only if device 1 is not requesting an interrupt.
If device 1 has a pending interrupt, it blocks the acknowledge signal from the next device by placing a 0 in the PO output.